## Slide 1
Roland Avenue Cycle Track Meeting
June 14, 2018

## Slide 2
Roland Avenue Safety Enhancement Design Options
Project Area
Design Option Illustrations
1
2
3
4
5
 | Reduces Car-Door/Bicycle Conflicts | Provides Separated Bike Facility | Provides Curbside Parking | Reduces Vehicle Parking/ Travel Lane Conflicts | Encourages Reduction of Vehicle Speed | Reduction in Travel Lanes | 2018 Implementation | Less Than $250,000
Option 1 (preferred): Widen Parking lane, reduce travel lanes from two lanes to one in both directions |  |  | X |  |  |  |  | 
Option 2: Remove parking protected cycle track, curbside parking, bike lane alongside parked cars, maintain two travel lanes in both directions | X | X |  |  | X | X |  | X
Option 3: Remove parking protected cycle track, curbside parking, install buffered bike lane alongside parked cars, reduce travel lanes from two lanes to one in both directions |  | X |  |  |  |  |  | X
Option 4: Remove parking protected cycle track, curbside parking, northbound median running two-way flex post or curb delineated cycle track, southbound buffered bike lane alongside parked cars, reduce travel lanes from two lanes to one in both directions |  |  |  | X |  |  | X | X
Option 5: Remove parking protected cycle track, curbside parking, median running one-way flex post or curb delineated cycle track, reduce travel lanes from two lanes to one in both directions |  |  |  | X |  |  | X | X
Cold Spring Lane
Northern Parkway
Deepdene Road
Project area
Full extents of bike lane
Notes: Remove all “pilot” language

## Slide 3
Widen the Parking Lane
  Reduce conflict between parked vehicles and travel lane
  Reduce conflict between parked vehicles and bicycle lane
  Create a safer more comfortable parking area
  Create a safer more comfortable bicycle lane
Reduce the Travel Lanes from Two Lanes to One in Both Directions
  Encourages reduction of vehicle speed
  Create a safer more comfortable parking area
  Create a safer more comfortable bicycle lane
Evaluate Impact on Traffic and Safety Concerns
Benefits and Trade-offs
Design Option 1 (Preferred Option)
 | Reduces Car-Door/Bicycle Conflicts | Provides Separated Bike Facility | Provides Curbside Parking | Reduces Vehicle Parking/ Travel Lane Conflicts | Encourages Reduction of Vehicle Speed | Reduction in Travel Lanes | 2018 Implementation | Less Than $250,000
Option 1: Widen Parking lane, reduce travel lanes from two lanes to one in both directions |  |  | X |  |  |  |  | 
ProjectArea
Cold Spring Lane
Northern Parkway
Deepdene Road
Project area
Full extents of bike lane

## Slide 4
Remove Parking Protected Cycle Track and Initiate Curbside Parking
  Reduces conflict between parked vehicles and travel lane
  Provides curbside parking
Install Bike Lane Alongside Parking Lane
  Provides a bike facility
Maintain Two Travel Lanes in Both Directions
Design Options 2 and 3
Project Area
Cold Spring Lane
Northern Parkway
Deepdene Road
Project area
Full extents of bike lane
 | Reduces Car-Door/Bicycle Conflicts | Provides Separated Bike Facility | Provides Curbside Parking | Reduces Vehicle Parking/ Travel Lane Conflicts | Encourages Reduction of Vehicle Speed | Reduction in Travel Lanes | 2018 Implementation | Less Than $250,000
Option 2: Remove parking protected cycle track, curbside parking, bike lane alongside parked cars, maintain two travel lanes in both directions | X | X |  |  | X | X |  | X
Option 3: Remove parking protected cycle track, curbside parking, install buffered bike lane alongside parked cars, reduce travel lanes from two lanes to one in both directions |  | X |  |  |  |  |  | X
Benefits and Trade-offs
Option 2
Remove Parking Protected Cycle Track and Initiate Curbside Parking
  Reduces conflict between parked vehicles and travel lane
  Provides curbside parking
Install Buffered Bike Lane Alongside Parking Lane
Reduce Travel Lanes from Two Lanes to One in Both Directions
  Encourages reduction of vehicle speed
  Create a safer more comfortable parking area
Option 3

## Slide 5
Remove Parking Protected Cycle Track and Initiate Curbside Parking
  Reduces conflict between parked vehicles and travel lane
  Provides curbside parking
Install Median Running Two-Way Cycle Track on Northbound Lane
  Provides separated bike facility
  Reduces conflict between parked vehicles and bicycle lane
Install Buffered Bike Lane on Southbound Lane
  Reduces conflict between parked vehicles and bicycle lane
Reduce Travel Lanes from Two Lanes to One in Both Directions
  Encourages reduction of vehicle speed
  Create a safer more comfortable parking area
Design Options 4 and 5
Project Area
Cold Spring Lane
Northern Parkway
Deepdene Road
Project area
Full extents of bike lane
Benefits and Trade-offs
Option 4
Option 5
Remove Parking Protected Cycle Track and Initiate Curbside Parking
  Reduces conflict between parked vehicles and travel lane
  Provides curbside parking
Install Median Running One-Way Cycle Track in Both Directions
  Provides separated bike facility
  Reduces conflict between parked vehicles and bicycle lane
Reduce Travel Lanes from Two Lanes to One in Both Directions
  Encourages reduction of vehicle speed
  Create a safer more comfortable parking area
  Create a safer more comfortable bicycle lane
 | Reduces Car-Door/Bicycle Conflicts | Provides Separated Bike Facility | Provides Curbside Parking | Reduces Vehicle Parking/ Travel Lane Conflicts | Encourages Reduction of Vehicle Speed | Reduction in Travel Lanes | 2018 Implementation | Less Than $250,000
Option 4: Remove parking protected cycle track, curbside parking, northbound median running two-way flex post or curb delineated cycle track, southbound buffered bike lane alongside parked cars, reduce travel lanes from two lanes to one in both directions |  |  |  | X |  |  | X | X
Option 5: Remove parking protected cycle track, curbside parking, median running one-way flex post or curb delineated cycle track, reduce travel lanes from two lanes to one in both directions |  |  |  | X |  |  | X | X

## Slide 6
Evaluation Results, Recent Progress, and Imminent Changes
Benefits and Trade-offs
Option 5
Evaluation Findings
Evaluation assessed vehicle speeds, cyclist behavior, and user/community perceptions of roadway conditions. Notable findings include:
Excessive speeds documented by Speed Sentry devices on Roland Avenue
People feel parking lanes and cycle track are too narrow
The majority of cyclists do use the cycle track
  A higher percentage use the cycle track in the northbound (uphill) direction
  A lower percentage use the cycle track in the southbound (downhill) direction – this is likely due to higher bicyclist speeds while traveling downhill
Traffic volumes are low, outside of peak hours
Recent Progress
The following changes to address community member concerns have been implemented in recent months:
Addressed Sight-Line Issues at Key Intersections
Restored Curbside Loading at Day School
Increased Traffic Enforcement Officer Presence
Implemented Speed Cameras and Speed Sentry Devices
Installed Stronger Flex Posts
Imminent Changes
Curbside Loading Sign
Speed Sentry
The following changes are scheduled for construction in 2018:
Curbside parking will be restored on the east side of Roland Avenue between Colorado Avenue and Deepdene Road
  An off-street bike path and a door-side buffered bike lane will both be installed in this segment

## Slide 7
Traffic Effects of Travel Lane Reduction
Option 5
Remove Parking Protected Cycle Track and Initiate Curbside Parking
  Reduces conflict between parked vehicles and travel lane
  Provides curbside parking
Install Median Running One-Way Cycle Track in Both Directions
  Provides separated bike facility
  Reduces conflict between parked vehicles and bicycle lane
Reduce Travel Lanes from Two Lanes to One in Both Directions
  Encourages reduction of vehicle speed
  Create a safer more comfortable parking area
  Create a safer more comfortable bicycle lane
A study was conducted to determine the traffic operations effects of a road diet on Roland Avenue. Traffic volumes were collected at the following intersections:
Roland Avenue at Cold Spring Lane
Roland Avenue at Wyndhurst Avenue
Roland Avenue at Deepdene Road
Intersection Data Collection
High Peak Hour Traffic Volumes
Traffic Analysis Results: Level of Service
Minor additional delays can be expected during the peak hours if a road diet is implemented.
 | AM Peak |  |  |  | PM Peak |  |  | 
 | Two Lane |  | One Lane |  | Two Lane |  | One Lane | 
Intersection | Average Delay(s) | Intersection LOS | Average Delay(s) | Intersection LOS | Average Delay(s) | Intersection LOS | Average Delay(s) | Intersection LOS
Deepdene Rd | 19.8 | B | 11.6 | B | 2.4 | A | 3 | A
Wyndhurst Ave | 24.9 | C | 44.8 | D | 15.2 | B | 23.3 | C
Cold Spring Ln | 77.8 | E | 80.8 | E | 113.7 | F | 113.7 | F
Predicted AM Peak Hour Queue Lengths After Lane Reduction
ROLAND AVENUE DEEPDENE ROAD
ROLAND AVENUE AT WYNDHURST AVENE
ROLAND AVENUE AT COLD SPRING LANE
Predicted PM Peak Hour Queue Lengths After Lane Reduction
ROLAND AVENUE AT COLD SPRING LANE
ROLAND AVENUE AT WYNDHURST AVENE
ROLAND AVENUE DEEPDENE ROAD
Predicted Travel Time Changes After Lane Reduction
 | AM Peak |  | PM Peak | 
 | Two Lane | One Lane | Two Lane | One Lane
Northbound (Cold Spring Lane to Northern Parkway) | 5 minutes | 6-7 minutes | 5 minutes | 6 minutes
Southbound (Northern Parkway to Cold Spring Lane) | 4 minutes | 5 minutes | 4 min | 4-5 minutes
Minor increases in travel time can be expected during the peak hours if a road diet is implemented.